## Slide 1: Trenching & Excavations Continuing Education Third Quarter 2017 Session 1

## Slide 2: Objectives
Upon completion of this module you should be able to:
  Explain the potential hazards of working in excavations
  Describe the various types of protective systems
  Understand the importance of evaluating site conditions and planning for them
  Define the role of the T&E competent person
  Describe inspection requirements
Notes: This presentation will provide you with an overview of the 1926 Subpart P standard on excavations. This will not serve as competent person training on this topic.
The discussion of this topic covers four main points.
At the conclusion of the training, you should be able to:
  State the greatest risk that is present in an excavation.
  Briefly describe the three main methods for protecting employees from cave-ins.
  Name at least three factors that pose a hazard to employees working in excavations, and at least one way to eliminate or reduce each of the hazards.
  Describe the role of a competent person at an excavation site and their responsibilities.

## Slide 3: Definitions
Excavation
  Any man-made cut, cavity, trench, or depression formed by earth removal.
Trench
  a narrow excavation. The depth is greater than the width, but not wider than 15 feet.
Notes: Reference 1926.650
Excavation: means any man-made cut, cavity, trench, or depression in an earth surface, formed by earth removal.
Trench/Trench excavation: means a narrow excavation (in relation to its length) made below the surface of the ground. In general, the depth is greater than the width, but the width of a trench (measured at the bottom) is not greater than 15 feet (4.6 m). If forms or other structures are installed or constructed in an excavation so as to reduce the dimension measured from the forms or structure to the side of the excavation to 15 feet (4.6 m) or less (measured at the bottom of the excavation), the excavation is also considered to be a trench.

## Slide 4: Excavation Safety
One of the most hazardous job task performed in construction
Around 70 fatalities each year
1000 injuries per year
Notes: Discuss that according to the U.S. Bureau of Labor Statistics (BLS) 271 workers died in trenching or excavation cave-ins from 2000 through 2006. A review of multiple national databases by NIOSH researchers found that trenching and excavation hazards during construction activities resulted in 488 deaths between 1992 and 2000 - an average of 54 fatalities each year. Sixty-eight percent of those fatalities occurred in companies with fewer than 50 workers. Forty-six percent of the deaths occurred in small companies with 10 or fewer workers. Hazards associated with trench work and excavation are recognized and preventable, yet injuries and fatalities associated with these hazards continue to occur. Regulations and consensus standards describe engineering controls, protective equipment, and safe work practices to minimize hazards for workers during trench work and excavations.

## Slide 5: Excavation Hazards
Cave-ins
Asphyxiation
Toxic materials
Fire
Equipment
Underground utilities
Did you know?
The fatality rate for excavation work is 112% higher than the rate for general construction.
Notes: Cave-ins are the greatest hazard from excavations.
However, other hazards such as asphyxiation due to lack of oxygen, inhalation of toxic materials, fire, overhead hazards from moving machinery near the edge, and underground utilities.
Its important to follow requirements for Dig-safe, One-call or other programs to insure you know about any underground utilities that may be in the area.

## Slide 6: Soil Weight
One cubic foot of soil weighs approximately 100 pounds
That’s 2700 pounds per cubic yard
Notes: Discuss that this is typical weight.
The addition of water in the soil, or heavy loams or clays can greatly increase this weight.
This much weight on your chest will prevent you from breathing.

## Slide 7: Site Evaluation and Planning
Soil conditions
Protective systems
Atmospheric hazards
Access/egress
Underground utilities
Structures
Notes: As with any part of the job, preplanning is an important step.
Before beginning an excavation, the competent person should evaluate the soil conditions, protective systems to be used, determine if atmospheric hazards could possibly be present, determine how employees will access the excavation, are there any underground utilities present and are there any structures that will be undermined.

## Slide 8: Protection of Employees
Employees shall be protected from cave-ins by using an adequately designed protective system or by sloping or benching the excavation
Protective systems must be able to resist all expected loads to the system
Notes: Protection of employees can be provided through use of a protective system or by sloping or benching the walls of the trench to prevent cave-in. There are different requirements based on soil classification.
This system is a method of protecting employees from cave-ins, from material that could fall or roll from an excavation face or into an excavation, or from the collapse of adjacent structures.

## Slide 9: Competent Person
Must have specific training
Knowledgeable about:
  Soils classification
  The use of protective systems
  The requirements of the standard
Must be capable of identifying hazards
Authorized to immediately eliminate hazards
Notes: Throughout the program we talk about a competent person. A competent person in excavation is a person who has specific training in, and who is knowledgeable about:
  Soil classification;
  The use of protective systems; and
  The requirements of the OSHA standard (Subpart P).
This person must also be capable of identifying hazards and has the authority to eliminate those hazards. If the person does not have the authority to take corrective action; they are not a competent person.

## Slide 10: Inspections of Excavations
A competent person must make daily inspections of excavations, areas around them and protective systems:
  Before work starts and as needed
  After rainstorms, high winds or other occurrence which may increase hazards, and
  When you can reasonably anticipate an employee will be exposed to hazards
Notes: Daily inspections of excavations, the adjacent areas, and protective systems shall be made by a competent person for evidence of a situation that could result in possible cave-ins, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions.
An inspection shall be conducted by the competent person prior to the start of work and as conditions change throughout the shift.
Inspections shall also be made after every rainstorm or other hazard increasing occurrence.
These inspections are only required when employee exposure can be reasonably anticipated.

## Slide 11: Inspections of Excavations
If the competent person finds evidence of a possible cave-in, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions:
  Exposed employees must be removed from the hazardous area
  Employees may not return until the necessary precautions have been taken
Notes: Where the competent person finds evidence of a situation that could result in a possible cave-in, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions, exposed employees shall be removed from the hazardous area until the necessary precautions have been taken to ensure their safety.