## Slide 1: Trenching & Excavations Continuing Education Third Quarter 2017 Session 3

## Slide 2: Trench Hazards
Notes: Introduce the module

## Slide 3: Injury and Death
Unprotected trenches and excavations can be hazardous
Most accidents occur in trenches 5-15 feet deep
There may be no warning before a cave-in
Notes: Year after year, excavations are one of the most hazardous construction operations.
Most accidents occur in the depth range of 5 to 15 feet.
Thus the requirement for protective systems at 5 feet.
Usually there are no warning signs that a trench is going to cave in.

## Slide 4: Protection from Falls, Falling Loads, and Mobile Equipment
Install barricades
Hand / mechanical signals
Grade soil away
Fence or barricade trenches left overnight
Use a flag person when signs, signals and barricades are not enough protection
Notes: To protect employees from these hazards, OSHA requires the employer to take the following precautions:
Keep materials or equipment that might fall or roll into an excavation at least 2 feet from the edge of excavations, or have retaining devices, or both.
Provide warning systems such as mobile equipment, barricades, hand or mechanical signals, or stop logs, to alert operators of the edge of an excavation. If possible, keep the grade away from the excavation.
Provide scaling to remove loose rock or soil or install protective barricades and other equivalent protection to protect employees against falling rock, soil, or materials.
Prohibit employees from working on faces of sloped or benched excavations at levels above other employees unless employees at lower levels are adequately protected from the hazard of falling, rolling, or sliding material or equipment.
Prohibit employees under loads that are handled by lifting or digging equipment. To avoid being struck by any spillage or falling materials, require employees to stand away from vehicles being loaded or unloaded. If cabs of vehicles provide adequate protection from falling loads during loading and unloading operations, the operators may remain in them.

## Slide 5: Protection from Falling Objects
Don’t operate equipment above workers
Maintain equipment distance from the edge by using warning systems spotters or stop logs
Notes: To protect employees from these hazards, OSHA requires the employer to take the following precautions:
Provide warning systems such as mobile equipment, barricades, hand or mechanical signals, or stop logs, to alert operators of the edge of an excavation. If possible, keep the grade away from the excavation.
Install protective barricades and other equivalent protection to protect employees against falling rock, soil, or materials.
Prohibit employees from working on faces of sloped or benched excavations at levels above other employees unless employees at lower levels are adequately protected from the hazard of falling, rolling, or sliding material or equipment.
Prohibit employees under loads that are handled by lifting or digging equipment. To avoid being struck by any spillage or falling materials, require employees to stand away from vehicles being loaded or unloaded. If cabs of vehicles provide adequate protection from falling loads during loading and unloading operations, the operators may remain in them.
When mobile equipment is operated adjacent to an excavation, or when such equipment is required to approach the edge of an excavation, and the operator does not have a clear and direct view of the edge of the excavation, a warning system shall be utilized such as barricades, hand or mechanical signals, or stop logs.
Prevent exposure to trench/excavation by the public during off hours by barricading, fencing or covers.

## Slide 6: Means of Egress
A stairway, ladder, or ramp must be present in excavations that are 4 or more feet deep
25 feet lateral travel distance from the employees
The ladder should extend 3 feet above the top of the excavation
Notes: Note the Trapped Worker!
At a depth of 4 feet, you must provide a means of access and egress from the excavation that allows no more than 25 feet of lateral movement for an employee to reach. This is accomplished through use of a ladder or ramp.
Structural ramps that are used solely by employees as a means of access or egress shall be designed by a competent person. Structural ramps used for equipment shall be designed by a competent person qualified in structural design, and shall be constructed in accordance with the design.

## Slide 7: Access and Egress
These two lashed together ladders are not an adequate means of egress
The ladder should extend 3 feet above the top of the excavation
Notes: Ladders must extend a minimum of 3 feet above the level being accessed.
[Discussion – Discuss the problems in the picture.]

## Slide 8: Other Excavation Hazards
Water accumulation
Oxygen deficiency
Toxic fumes
Access/Egress
Falls
Notes: Some other hazards can be:
  Water accumulation;
  Oxygen deficiency;
  Toxic fumes;
  Access/egress; and
  falls

## Slide 9: Water is Hazardous
Water in an excavation is hazardous
Employees cannot work in an excavation where:
  Water has accumulated
  Water is accumulating
Notes: Employees shall not work in excavations in which there is accumulated water, or in excavations in which water is accumulating, unless adequate precautions have been taken to protect employees against the hazards posed by water accumulation.
The precautions necessary to protect employees adequately vary with each situation, but could include special support or shield systems to protect from cave-ins, water removal to control the level of accumulating water, or use of a safety harness and lifeline.
If water is controlled or prevented from accumulating by the use of water removal equipment, the water removal equipment and operations shall be monitored by a competent person to ensure proper operation.

## Slide 10: Hazardous Atmosphere
Test excavations more than 4 feet deep before an employee enters the excavation for:
  Oxygen deficiency
  High combustible gas concentration
  High levels of other hazardous substances
Notes: In excavations where a hazardous atmosphere could reasonably be expected to exist, the atmosphere must be tested the same as a confined space. Some examples of where this may be needed is when digging in a landfill, chemical plant, or an area that has contaminated soils.
If hazardous conditions exist, controls such as proper respiratory protection or ventilation must be provided. Also, controls used to reduce atmospheric contaminants to acceptable levels must be tested regularly.
Where adverse atmospheric conditions may exist or develop in an excavation, the employer also must provide and ensure that emergency rescue equipment, (e.g., breathing apparatus, a safety harness and line, basket stretcher, etc.) is readily available. This equipment must be attended when used.
Employees shall not be permitted to work in hazardous and/or toxic atmospheres. Such atmospheres include those with:
  less than 19.5% oxygen,
  a combustible gas concentration greater than 10% of the lower flammable limit, and,
  concentrations of hazardous substance that exceed those specified in the Threshold Limit Values for airborne contaminants established by the ACGIH.

## Slide 11: Dig Safe
Notes: Discuss that before digging, the presence of, and the estimated location of underground utilities must be determined per local requirements.

## Slide 12: At Risk?
No Cave-in Protection
Close proximity of equipment
Spoil pile too close
No ladder
Unsupported utilities
No head protection
Suspended load
Fall Hazard
Notes: In addition to an unprotected trench, a cave-in hazard is increased by machinery which gets too close.
Even normal vehicular traffic, such as that along an adjacent interstate or road through an industrial park may impact an excavation. The vibrations from continuous or heavy traffic may undermine the soil and cause a cave-in.
[Discussion]
Discuss other safety concerns in this picture.
  Spoil pile
  Working under suspended loads
  Unsupported utilities
  No ladder
  No head protection
  Fall Hazard