## Slide 1: Manual Material Handling
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
3RD QUARTER 2024

## Slide 2
OBJECTIVES – Q3 MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Identify common causes of manual material handling injuries.
Understand specific methods and best practices for safely performing manual material handling.

## Slide 3: PART 1 of 2: COMMON CAUSES Of manual material handling injuries

## Slide 4
Q3 - MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
(6) COMMON CAUSES OF INJURIES:
Overexertion Injuries: Overexertion from lifting, lowering, or carrying heavy materials is a leading cause of material handling injuries and musculoskeletal disorders (MSD).
Struck-by accidents: Workers can be struck by materials being dropped from heights or falling from unprotected edges.
Caught-in or caught-between accidents: Workers can be crushed or pinned due to being caught in or between materials during manual material handling.
…continues on next slide

## Slide 5
Q3 - MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
(6) COMMON CAUSES OF INJURIES (continued):
Falls: Falls from elevated surfaces while handling materials, such as structures, ladders, or equipment, are a significant risk.
Repetitive motion: Over time, continuous handling of materials with poor ergonomic care can lead to musculoskeletal disorders.
Lack of using proper equipment (or incorrect use): Opting to manually handle material when there is a superior mechanical option, can result in injuries. Likewise, incorrect use of equipment can result in injury or damage to equipment or property.

## Slide 6: Injury Causes #1: Overexertion
In many cases, overexertion injuries are the result of a single incident, such as lifting a weight that is designed for more than one person.
Almost half (41%) of all construction injuries are a result of overexertion.
Days away from Work in construction are approx. 70% due to sprains, strains and tears, mostly to the upper body.
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
6
Notes: Overexertion and bodily reaction injuries and illnesses resulted in the most DART cases and the second most DAFW cases during 2021-2022.
Data is from 2021-2022. Source: Work Safety: Overexertion and Bodily Reaction - Injury Facts (nsc.org)

## Slide 7: Injury Causes #1: Overexertion
WORST OFFENDER:
BACK INJURY
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
7
Every Year:
  Back injuries make up 25% of all injuries reported.
  A back injury causes 1 out of every 100 workers to miss work.
    Workers with back/neck injuries lose an average of 7 work days, and sometimes more than 30.
  Careers in construction often end prematurely, due to permanent damage resulting from repeated back injuries.
Notes: Most back problems are low-back injuries, including sprains and strains from lifting, lowering, carrying, pushing and pulling materials. You are at higher risk of low-back injury if you often carry heavy loads, must twist while carrying heavy loads, or work a lot while bent over or in other awkward postures.
Sources
https://www.work-fit.com/blog/3-statistics-on-back-injuries-in-the-workplace-every-boss-should-know
https://www.safemt.com/resources/tips-for-preventing-back-injuries-in-construction/

## Slide 8: MUSCULOSKELETAL DISORDERS (MSD) Resulting from overexertion
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Repetitive Motions
Awkward Positions
Vibration (tools)
Contact Stress
Vibration
Injury Causes #1: Overexertion
Notes: Risk for MSD increases with these types of hazards:
Repetition- same task or muscles used repeatedly AND NOT ALLOWED TO REST. Repetitive lifting of light objects can be just as damaging as lifting a single heavy object
High Force Exertion - high muscle power in lifting & gripping
Awkward Postures- muscles / joints bent out of normal position, such as: Working with your hands over your head, Bending your neck or back, Kneeling or squatting, Twisting at the waist
Contact Stress- pressure pressed on small body area (examples: palm, knee, or forearm). Most common ergonomic hazard in construction work. Working with hand tools can also cause contact stress. Hand Tools with no padded grips, tools with finger-grooves. Suggest providing padded gloves and getting updated hand tools
Vibration-from power tools or equipment; Hand-Arm; Continuous use of power tools can cause MSD’s. Vibration from these tools can damage blood vessels and nerves in your arms and hands.

## Slide 9: HOW TO RECOGNIZE MUSCULOSKELETAL DISORDERS (MSD)
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
WARNING SIGNS:
Weakened grip strength
Decreased range of motion
Loss of muscle function
Injury Causes #1: Overexertion
SYMPTOMS:
Pain
Stiffness
Numbness
Burning or Tingling
Notes: Risk for MSD increases with these types of hazards:
  Repetition- same task or muscles used repeatedly
  High Force Exertion - high muscle power in lifting & gripping
  Awkward Postures- muscles / joints bent out of normal position
  Contact Stress- pressure pressed on small body area (examples: palm, knee, or forearm)
  Hand-Arm Vibration-from power tools or equipment

## Slide 10: WHEN SHOULD YOU REPORT MSD SYMPTOMS?
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
  Pain is severe
  Pain becomes worse over time
  Symptoms include numbness or tingling
  Discomfort keeps you awake at night
Injury Causes #1: Overexertion
Notes: An ergonomic evaluation may be ordered:
  1. Evaluate the task / process – is the part that causes pain necessary? Can it be changed?
  2. Evaluate the tools used for the task. Is it the proper tool? Is it in good working condition?
When symptoms are reported early, equipment or process changes could eliminate the issue causing the discomfort. The muscles can then RECOVER naturally from the injury – like traumatic muscle injuries
OTHER TREATMENTS MAY INCLUDE:
Anti-Inflammatory Medications – Injections and/or Internally Taken
Occupational & Physical Therapy to Strengthen Muscles
Chiropractic Care
Therapeutic Massage
In Extreme Cases - Surgery

## Slide 11: Injury/Incident Causes #2: Struck-By
DROPPED OBJECTS
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
11
EQUIPMENT HAZARDS WHILE MOVING MATERIAL
COMMON OFFENDERS:
Struck-by while handling material
MATERIAL NEAR
UNPROTECTED EDGES

## Slide 12: Injury/incident Causes #2: Struck-By
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
12
DROP ZONE DANGERS:
Head/arm injuries from falling material (drop-zone, demo work, throwing out trash)
Foot injuries from dropped loads
Mechanical failures (broken sling or sudden load shifting)
Heavy winds or weather causing material to move or slip
DROP
ZONE

## Slide 13
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
13
HOW HEAVY IS “DEADLY”?
Just 1 pound from 6 feet can cause a serious injury.
5 pounds from just 10 feet can be Severe.
Just 10 pounds from 20 feet can be severe to DEADLY.
Injury/Incident Causes #2: Struck-By Material
Notes: A sharp, one-pound object falling from 6 feet can easily cause a laceration or worse.
Falling objects pose an inherent risk for struck-by injuries on the job site. Tools, materials, and other objects can fall from roofs, cranes, and scaffolds, but even objects falling from lower levels such as a truck bed or dolly can lead to injuries. Several factors increase the risk of more severe injuries including the shape of the object and where on the body the person is struck. The height at which the object falls and weight of the object are also extremely important, with injury severity increasing as the height and weight of the falling object increase.
Source; https://blogs.cdc.gov/niosh-science-blog/2023/04/04/2023-struck-by-stand-down/

## Slide 14: Injury causes #3: Caught in or Caught-Between Material
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
14
Trying to free jammed/stuck material with body parts in line-of-fire
Crushing injuries while placing or moving materials with heavy equipment (trucks, forklift, cranes)
Shifting material due to poor staging, unbalanced load, weather conditions, etc.
COMMON OFFENDERS (caught in/caught between):

## Slide 15: Injury causes #3: Caught in or Caught-Between Material
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
15
Getting injured due to being caught in or between material/equipment doesn’t necessarily require a major equipment failure or operator error.
Material handling injuries can happen during routine, simple tasks. For example, having your hands in the wrong place under weight of a heavy insulator, or adjusting the fork widths on a forklift, or not watching for your co-worker’s hand placement.

## Slide 16
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Obstructed view due to large material
Messy work site
Uneven surfaces
Open holes
Handling obscure objects
Icy/wet conditions
Working atop equipment (Wire trailers, pulling equipment, etc.)
Injury/Incident Causes #4: Falls
COMMON OFFENDERS
(Falls while handling materials manually):

## Slide 17: Injury causes #5: Repetitive Motion
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
17
COMMON OFFENDERS
(repetitive motion):
Tendinitis: Inflammation due to repetitive gripping or overhead tasks.
Rotator Cuff Injuries: Strain or tears from overhead lifting or reaching.
Epicondylitis: Elbow tendon inflammation from repetitive motions.
Carpal Tunnel Syndrome: From repetitive hand tool use, causing wrist nerve compression.
Notes: Tendinitis commonly affects workers who perform tasks requiring repetitive gripping or overhead reaching, such as using jackhammers or painting. It involves inflammation of the tendons and can cause pain, swelling, and restricted movement.
Rotator Cuff Injuries: Often seen in construction workers who repeatedly lift heavy objects overhead or perform tasks with extended reach, leading to strain and tears in the muscles and tendons of the shoulder. Symptoms include pain, weakness, and limited range of motion in the shoulder.
Epicondylitis (Tennis Elbow/Golfer's Elbow): Resulting from repetitive motions like swinging a hammer or using a screwdriver, causing inflammation of the tendons in the elbow. Symptoms include pain and tenderness on the outside (tennis elbow) or inside (golfer's elbow) of the elbow joint.
Carpal Tunnel Syndrome is Often caused by repetitive use of hand tools such as hammers and drills, leading to compression of the median nerve in the wrist. Symptoms include numbness, tingling, and weakness in the hand and wrist.

## Slide 18
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Failure to use the right tool for the task
  Would a chainfall, come-along, or other rigging system help?
  Would a dolly, pallet jack, forklift, crane, or other method save your back or hands from strains?
  Overconfidence: “I’ve lifted heavier objects before.”
Injury/Incident Causes #6:
Lack of/Improper use of equipment
COMMON OFFENDERS
(Lack of/Improper use of equipment):

## Slide 19: PART 2 of 2: BEST PRACTICES Specific Methods for Safe Manual Material Handling

## Slide 20: Best practices: OVEREXERTION
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Implement breaks during strenuous tasks to allow muscles to recover from lifting or tight gripping
Mechanically lift/leverage/tie down materials that are awkward or heavy.
Use mechanical aids to move items around; use dollies, hand trucks, carts, etc.
Pay attention to body positioning for best ergonomic relief.
Notes: To prevent overexertion injuries in construction, workers should prioritize proper lifting techniques, including bending the knees and keeping the back straight when lifting heavy objects. Additionally, using mechanical aids such as dollies or forklifts can reduce the strain on the body. Implementing regular breaks during strenuous tasks allows muscles to rest and recover. Adequate training on ergonomics and the importance of proper posture can help workers maintain optimal body mechanics throughout their tasks. Furthermore, rotating job tasks among workers can prevent overuse of specific muscle groups. Finally, maintaining overall physical fitness and flexibility through regular exercise can enhance resilience against overexertion injuries on construction sites.

## Slide 21: Best Practices: OVEREXERTION
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Make sure the crew is trained on proper lifting
Incorporate a stretch-and-flex program prior to work and after breaks.
2-person lift if it’s awkward or over 50 lbs!

## Slide 22: Best Practices: OVEREXERTION
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Implement a Stretch-and-Flex program to combat Musculoskeletal Disorders (MSD)

## Slide 23: Best Practices: Stretch-and-Flex
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Trunk and Low Back Stretches

## Slide 24: Best Practices: Stretch-and-Flex
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Upper Body Stretches

## Slide 25: Best Practices: Stretch-and-Flex
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Leg Stretch

## Slide 26: OVEREXERTION: how to save your back
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Assess the weight and stability of the object before lifting.
Don’t overestimate your abilities!
Notes: Proper lifting techniques are crucial for construction workers to prevent injuries and maintain long-term physical health. Before lifting any object, it's essential to assess its weight and stability. To lift safely, workers should bend at the knees, keeping the back straight, and engage the leg muscles to lift the load. Keeping the load close to the body reduces strain on the back. Additionally, workers should avoid twisting while lifting or carrying heavy objects, as this can lead to strain or injury to the spine. Utilizing mechanical aids like dollies or forklifts for heavier items can also reduce the risk of injury. Regular training and reinforcement of proper lifting techniques are vital to ensure that construction workers prioritize their safety and well-being on the job.
Photo Credit: http://wc1.smartdraw.com/examples/content/Examples/10_Healthcare/Orthopedics/Posture_Proper_Lifting_Technique_L.jpg, Accessed 2/8/11

## Slide 27: OVEREXERTION: how to save your back
Q3 2024 – MANUAL MATERIAL HANDLING – BEST PRACTICES
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Break load into parts
Get help with heavy or bulky items
Lift with legs, keep back straight, do not twist
Use handling aids - such as steps, trestles, shoulder pads, handles, and wheels
Avoid lifting above shoulder level

## Slide 28: STRUCK-BY INJURY AVOIDANCE
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
When people have the potential to work above crew areas, establish drop-zone barricades/barriers and discuss procedures in the daily job briefing.

## Slide 29: STRUCK-BY INJURY AVOIDANCE
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
Material can fall from unstable edges of any surface.
  Trenches
  Underground Vault Openings
  Structures
  Equipment
Be sure material is secured and/or stored away from workers below open holes and leading edges.

## Slide 30: Stay out of the bite!
Don’t let material handling distract you from pinch points.
Don’t put yourself between moving equipment or material and objects.
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
30
CAUGHT-BETWEEN
INJURY AVOIDANCE

## Slide 31
Consider the (6) common types of injuries with material handling :
    Overexertion
    Struck-By
    Caught-Between
    Falls
    Repetitive Motion
    Lack of proper tool/incorrect use
Use tools to prevent injury:
    Allow muscles to recover
    Use mechanical means
    Pay attention to body position
    Get training on proper lifting
    Stretch-and-Flex
    2-person lift for heavy or awkward items
    Establish and respect drop zones
    Stay out of the bite!
Q3 2024 – MANUAL MATERIAL HANDLING
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
31
REVIEW

## Slide 32: Thank You!

## Slide 33: Manual Material Handling
OSHA ELECTRICAL TRANSMISSION & DISTRIBUTION PARTNERSHIP
3RD QUARTER 2024