## Slide 1: Insulate and Isolate
000
Practical Scenario

## Slide 2: Proper Insulate & Isolate
Crew tasked with changing cut out. They have permission to take an outage on the transformer, but the primary must stay energized
Identify ALL Insulate and Isolate opportunities

## Slide 3
000
Notes: The presenter will describe the scene and the job, this is a multi-circuit 12470v system with a single-phase transformer. The job is to change out the cutout, both primary circuits must remain energized, but the transformer can be de-energized. So what do we do first? Insulate or Isolate?

## Slide 4
000
Insulate
Notes: Presenter will discuss Insulating is first as it offers protection to the worker for the remainder of their work.

## Slide 5
000
Insulated
Notes: Presenter to go over Proper Insulation
Crew Members are wearing properly rated Gloves and Sleeves from Cradle to Cradle
Overhead phases are covered on the way into the work zone and only uncovered once the job is finished and on the way out of the work zone.
Insulator covers are used to prevent any inadvertent contact
A blanket is placed on the arm to protect any second point of contact
Insulation is applied to the CrossArm brace and Neutral

## Slide 6
000
Isolate
Notes: Now that the work zone is insulated we will look at Isolation opportunities

## Slide 7
Isolated
Notes: Presenter to go over Proper Isolation
Cutout opened with approved Load Break tool
High Side jumper removed and coiled up
Bottom jumper from transformer to cutout removed and coiled up
Lightening Arrestor jumper removed and coiled up

## Slide 8
000
Notes: Once the work is complete, we simply reverse the isolation and Insulation process. Additional items to keep in mind:
Live Line Tools can be used to prevent workers approaching MAD
Always keep Extended Reach in mind